## Slide 1: International Dynamics of EMF Natural Gas Scenarios MF 31.4 North American Natural Gas Markets in Transition
Sonia Yeh, University of California, Davis
Yiyong Cai, CSIRO Oceans & Atmosphere Flagship
Daniel Huppman & Franziska Holz, German Institute for Economic Research
Paul Bernstein, Sugandha Tuladhar, NERA Economics
May 7th and May 8th, 2015
Washington, DC

## Slide 2: Motivations
Several studies (e.g. NERA, EIA, Baron et al. 2015) look at the impacts of US exports (e.g. 6 TCF, 12 TCF, unlimited) on US production, GDP and global gas prices
  EIA examined scenario of 7.3 TCF/yr exports, found LNG exports increase price by -4% to 14% ; GDP increase 0.05%-0.17%
  Baron et al. (2015) shocked the international market with higher Asian demand using NewERA model assuming production restraint in non-US regions.
    LNG exports up to 12.8 TCF, positive GDP impacts
    Less US advantage when non-US production restraint was removed.
Using relatively simple regional supply and demand curves and elasticity assumptions to represent international responses

## Slide 3: Scenarios
Name | Description
#1. Reference | US results calibrated to AEO 2014; International results calibrated to IEO 2013.
#2. High Shale (HR) | Follow AEO 2014 High Resource Case
#6. High Asian Demand (HAD) | Expand the Asian demand for natural gas by approximately 20% (7-11 TCF) in 2040
#7. High Demand High (HAD+HR) | Combine #2 and #6
GTEM-C  CSIRO, Australia (Computable General Equilibrium)
DIW-MFM  German Institute for Economic Research (Spatial Equilibrium)
GNGM  NERA, Inc. (Spatial Equilibrium)

## Slide 4: Summary of Findings
Higher Asian Demand (7-11 TCF in equilibrium in 2040) alone leads to 0.02 – 1.02 TCF increase in US production in 2040.
  Mixed results in production changes from other countries
  Mainly Russia and Middle East will increase exports; NERA: US, Africa, Oceania
US High Shale lowers US & world gas prices,
  NERA&DIW: lowers production elsewhere; or
  GTEM-C: lower gas prices increases GDPs and demands for gas in other countries, thus increases productions elsewhere.
US High Shale may or may not affect US demand
  Understand the fundamental drivers for US demand is more important than resource shock

## Slide 5: High Shale Scenario – Production Change
NERA-GNGM &DIW: Production increase in US; decreased production in all the other countries
GTEM-C: Gas production dropped in most other regions in the short term. Income effects due to lower gas prices will increase GDP and the demand for gas in the rest of the world, and it consequently increases production elsewhere